   Assignment
        NAND & NOR Flash Memory
    - S. Stalin Srinivasan ( 0756 )
Flash Memory:

Flash memory has become a powerful and cost-effective solid-state storage technology widely used in mobile electronics devices and other consumer applications. Some kind of non-volatile memory is necessary for computing systems so that the system does not erase all data every time it is powered down, or following a power failure . Two major forms of Flash memory, NAND Flash and NOR Flash .

NAND _ NOR Flash:

        NAND Flash, which was designed with a very small cell size to enable a low cost-per-bit of stored data, has been used primarily as a high-density data storage medium for consumer devices such as digital still
cameras and USB solid-state disk drives.
        NOR Flash has typically been used for code storage and direct execution in portable electronics devices, such as cellular phones and PDAs.
        NAND Flash has become an attractive alternative for the data storage aspects of today’s cell phones because of its higher speed write and erase performance as well as its low cost-per-bit. As a result, designers of memory subsystems in portable electronics are now using NAND in some traditional NOR-based applications. For today’s full-featured cell phones, many designers are utilizing memory architectures that combine NOR with NAND for data storage in which different types of memories are frequently stacked in Multi-Chip Packages (MCP) to create a single component.

Memory Architecture:

        In NOR flash configuration, the individual memory cells are connected in parallel, which enables the device to achieve random access. NOR Flash is ideal for lower-density, high-speed read applications, which are mostly read only, often referred to as code-storage applications.

      In NAND flash configuration an array of eight memory transistors connected in a series. Utilizing the NAND Flash architecture’s high storage density and smaller cell size, NAND Flash systems enable faster write and erase by programming blocks of data. NAND Flash is ideal for low-cost, high-density, high-speed program/erase applications, often referred to as data-storage applications.

Flash Density:

        In theory, the highest density NAND will be at least twice the density of NOR, for the same process technology and chip size. In reality, market forces determine the highest density that will be commercially produced. Today, comparing only single chip memory
with one bit per cell (also called Single Level Cell, or SLC), the highest density NOR commercially available is 256 megabit1 (Mb), while NAND is available in densities of 4 gigabit2 (Gb). Because cost-per-bit, which is closely related to the silicon real estate required, is one of the most important characteristics of memory, the small cell size characteristic of NAND Flash is a significant factor.

Multi Chip Package (MCP):

MCPs can combine NAND Flash, NOR
Flash memory, Pseudo SRAM and/or low power DRAM in a single package by using chip- stacking technology. This technology enables a complete memory subsystem with different types of semiconductor memory to be packaged as a single component to reduce size and contribute to cost reduction for cellular phones and other portable devices.